## Slide 1
LInOG FBS + FBD InSAR processing workflow
ALOS-1 PALSAR, pipeline v4.0, one frame: each phase (left) and its output (right); read left to right, row by row.
Phase 0
Set-up and pre-flight
Install ISCE2, MintPy, GDAL, SNAPHU; check provenance; size the machine; count the archive
provenance check
OUTPUT
Verified processing environment
Software checked, parallel settings sized, scene count matched
Phase 1
Unpack and unify FBS + FBD
Unzip L1.1 granules; beam check; sort FBS / FBD; band-limit FBS to 14 MHz at native 4.68 m range sampling
gates G1–G6
NEW IN YEAR 2
OUTPUT
One unified SLC stack
All dates at one 14 MHz bandwidth; 19–24 dates per frame
Phase 2
DEM and network design
Shared DEM; pairs with temporal baseline ≤ 730 d and perpendicular baseline ≤ 1,500 m
gate G17
OUTPUT
DEM + interferogram network
Pair list and run files (123–180 pairs formed per frame)
Phase 3
Coregistration
Align every SLC to one FBS reference date (4.68 m range grid; FBD resampled onto it)
gates G7–G9, G16, G21
OUTPUT
Coregistered SLC stack
All acquisitions on the reference geometry
Phase 4
Interferogram generation
Form interferograms; multilook 28 × 12 (~90 m × 90 m); filter; unwrap with SNAPHU
gates G10, G11, G18, G20
OUTPUT
Unwrapped interferograms
Interferograms and coherence for every admitted pair
Phase 4.5
Visual quality control
Phase and amplitude report pages for every interferogram
visual check
OUTPUT
Interferogram report grids
Poor pairs flagged and excluded
Phase 5
SBAS time-series analysis
MintPy inversion; DEM-error correction; ramp removal; coherence and water masks
gates G12, G13, G15, G19, G22, G23
OUTPUT
Displacement time series
LOS velocity, displacement per date, temporal coherence
Phase 6
Geocoding and delivery
Geocode to a common 1/1200° (~90 m) grid; 16 products per frame; 27-check verification
gate G14; 27 checks
OUTPUT
16 geocoded products per frame
LOS, vertical, horizontal GeoTIFFs; KMZ; hillshade maps
Phase 7
Interpretation
Read the velocity maps; measure subsidence against nearby stable ground
two-track check
OUTPUT
Ground-deformation results
e.g. Cabanatuan 4.4–4.7 cm/yr vertical, two tracks
new for FBS+FBD processing
carried over from FBS-only
output of the phase
Green italic: automated quality gates (G1–G23); a failed gate stops the phase.

## Slide 2
LInOG FBS + FBD InSAR processing workflow: real outputs
ALOS-1 PALSAR, pipeline v4.0, one frame: each phase (left) and its output (right); read left to right, row by row. Sample: Path 449 Frame 0280.
Phase 0
Set-up and pre-flight
Install ISCE2, MintPy, GDAL, SNAPHU; check provenance; size the machine; count the archive
provenance check
OUTPUT
# pre-flight record (felix, 17 Sep 2026)
provenance ... OK
ISCE2 · MintPy · GDAL · SNAPHU OK
48 cores, 125 GB RAM
779 ALOS-1 L1.1 zips
RESULT: PASS 14/14
Summary of the pre-flight record: all 14 checks pass
Phase 1
Unpack and unify FBS + FBD
Unzip L1.1 granules; beam check; sort FBS / FBD; band-limit FBS to 14 MHz at native 4.68 m range sampling
gates G1–G6
NEW IN YEAR 2
OUTPUT
Range spectra: FBS before / after band-limiting match FBD
Phase 2
DEM and network design
Shared DEM; pairs with temporal baseline ≤ 730 d and perpendicular baseline ≤ 1,500 m
gate G17
OUTPUT
Baseline network of the pairs, 2007–2011
Phase 3
Coregistration
Align every SLC to one FBS reference date (4.68 m range grid; FBD resampled onto it)
gates G7–G9, G16, G21
OUTPUT
Coregistration residuals per date
Phase 4
Interferogram generation
Form interferograms; multilook 28 × 12 (~90 m × 90 m); filter; unwrap with SNAPHU
gates G10, G11, G18, G20
OUTPUT
Filtered interferogram, 8 Jan – 23 Feb 2008
Phase 4.5
Visual quality control
Phase and amplitude report pages for every interferogram
visual check
OUTPUT
Report page used to inspect every pair
Phase 5
SBAS time-series analysis
MintPy inversion; DEM-error correction; ramp removal; coherence and water masks
gates G12, G13, G15, G19, G22, G23
OUTPUT
Network coloured by coherence; coherence matrix
Phase 6
Geocoding and delivery
Geocode to a common 1/1200° (~90 m) grid; 16 products per frame; 27-check verification
gate G14; 27 checks
OUTPUT
Delivered LOS velocity map (cm/yr)
Phase 7
Interpretation
Read the velocity maps; measure subsidence against nearby stable ground
two-track check
OUTPUT
Cabanatuan bowl, Path 448 and Path 449
new for FBS+FBD processing
carried over from FBS-only
output of the phase
Green italic: automated quality gates (G1–G23); a failed gate stops the phase.

## Slide 3
Progression of LInOG ground-velocity coverage, 2007–2011
ALOS-1 PALSAR ascending tracks, deramped LOS velocity, same ±5 cm/yr colour scale
YEAR 1 (reported June 2026)
FBS only · Path 448 · 5 frames
10 dates/frame · 34–36 interferograms/frame
~10,000 km² reported · no water mask
YEAR 2, QUARTER 2 (this report)
FBS + FBD · Paths 447–449 · 12 frames
19–24 dates/frame · 1,634 interferograms in total
27,893 km² with valid data · water-masked (v1.2)

## Slide 4
LInOG tutorial route on EarthScope GeoLab (manual v4.0, Chapter 11)
Browser-based JupyterLab server: trainees run the LInOG notebook on a four-date demonstration stack, without access to the project server
Step 1
EarthScope account
Google log-in to the GeoLab hub
Step 2
Start a server
29 GB profile: 3.66 CPU cores, 29,776 MiB memory
Step 3
One-time install
ISCE2, MintPy, GDAL, SNAPHU into home (~7 min)
Step 4
Demonstration stack
Path 449 Frame 0290: 4 dates, 6 pairs (2008)
Step 5
Run the notebook
Cells 0–18 call the LInOG scripts, Phases 0–6
Step 6
Check and deliver
18-item run check; 16 products
REAL OUTPUTS PRODUCED ON GEOLAB (September 2026; four-date demonstration stack, for training only)
Phase 4.5: interferogram report sheet (GeoLab, 20 Sept 2026)
Phase 5: velocity in radar coordinates (GeoLab, 22 Sept 2026)
Phase 6: delivered velocity map, cm/yr (GeoLab, 20 Sept 2026)